## Slide 1: MULTILEVEL INVERTER BASED ON SWITCHED-CAPACITANCE STRUCTURE
Guided By,
Prof. Sanish Kumar T G
Department of EEE
GEC Thrissur
Presented By,
Alin Anto(16) S7 EEE A
Abhilash M M(2) S7 EEE A
Don Dev(44) S7 EEE A
Devika Sajeev(40) S7 EEE A

## Slide 2: CONTENTS
Introduction
Existing System
Proposed System
Specific Requirements
Expected Outcome
Project Plan
References

## Slide 3: INTRODUCTION
Recently, multilevel inverters (MIs) are getting more attention from researchers because of advantages like better waveform quality, lower EM noise, and lower device stress.
MIs are used to couple a DC source to an AC bus for applications like electric motor drivers, uninterruptible power supplies, and distributed generation systems.

## Slide 4: EXISTING SYSTEM(Problem identification)
The following topologies are now used in practice:-
Neutral-point clamped (Diode clamped)
Flying capacitor
Cascaded H-bridge (CHB)
Disadvantages:
  Large number of components( switches, power supplies, capacitors, and diodes)
  Large size and high cost
  Complex control.
  For low-power applications, the system size and cost are the main concerns

## Slide 5: PROPOSED SYSTEM
Switched-capacitor (SC) structure is added to the H-bridge inverter .
The SC structures use capacitors, switches, and diodes to create a multilevel DC voltage at the DC bus of the H-bridge circuit.
H-bridge circuit inverts the multilevel DC voltage to AC voltage.
UNREGULATED DC
SWITCHED CAPACITOR STRUCTURE
MULTILEVEL DC
H-BRIDGE
REGULATED AC

## Slide 6: PROPOSED SYSTEM(Advantages)
Compared to conventional topologies, the proposed system has the following advantages:-
Boost operation without magnetic elements.
Fewer components(switches, sources & capacitors)
Smaller & less expensive.
Less complex control.
Requires only one power DC source
  For low-power applications, the system size and cost are the main concerns

## Slide 7: SPECIFIC REQUIREMENTS
Hardware Requirement :-
    DSO (Analysis)
    DSP (controller)
    Function generator (Analysis & reference)
Software Requirement :-
    MATLAB (Simulation)
    Proteus (Design)
    Tex studio (Documentation)

## Slide 8: EXPECTED OUTCOME
Literature survey
Mathematical model of SCMI
Design of 350W SCMI
Simulation studies
Prototyping
Performance Analysis
Improvements
Documentation

## Slide 9: PROJECT PLAN
SEMESTER VII
PHASE I
  Problem identification(October 2018)
  Formulating the Objective of the Project(October 2018)
PHASE II
  Literature Survey(November 2018)
  Modelling(November 2018)
SEMESTER VIII
PHASE I
  Design of Proposed System and simulation study(January 2019)
  Prototyping(February 2019)
PHASE II
  Performance Analysis and Improvements (March 2019)
  Conclusion and Documentation (March 2019)

## Slide 10: REFERENCE
[1] Bac-Bien Ngo, Minh-Khai Nguyen , Jae-Hong Kim2 and Firuz Zare, “Single-phase multilevel inverter based on switched-capacitor structure”, IET Power Electron, June 2018, ISSN 1755-4535
[2] Barry W Williams, “Principles and Elements of Power Electronics Devices, Drivers, Applications, and Passive Components”, 2006, ISBN 978-0-9553384-0-3
[3] Yuanmao Ye, K. W. E. Cheng, Junfeng Liu and Kai Ding, “A Step-Up Switched-Capacitor Multilevel Inverter With Self-Voltage Balancing”, IEEE Trans. Ind. Electron, Vol. 61, No. 12, December 2014
[4] Bhagyalakshmi P S, Beena M Varghese and Dr. Bos Mathew Jos, “Switched Capacitor Multilevel Inverter With Different Modulation Techniques”, International Conference on Innovations in information Embedded and Communication Systems, 2017